## Slide 1
AI for Earphone Shape Design
Knowledge, tools, and human reviews in the earphone design loop
Knowledge
find evidence
Generate
explore ideas
Execute
operate tools
Review
record lessons
Focus: AI participation, process iteration, and lesson reuse
Notes: We use a product design case to study how AI takes part in design tasks, and what reusable method each revision left behind. The case covers the earliest trial through the current candidate, organized in five stages. Knowledge retrieval supplies references, generation tools help compare concepts, execution tools perform the operations, and people together with check tools review the results. Design review and lesson write-back run through all of these steps. The report focuses on how AI participates, how the process changed, and what was verified.

## Slide 2
Design Features and Six Concepts
Seed Pod
Concept 1
Shallow saddle soft support
Pebble
Concept 2
Rounded low profile
Fin Wing
Concept 3
Short wide soft fin
Spiral
Concept 4
Shallow curled surface
Bloom
Concept 5
Petal soft-gel wrap
Twin Petal
Concept 6
Overlapping twin shells
Six left-ear concepts demonstrate this round's generation flow.
Input features set the generation direction. People compare and select.
同一需求下，AI 生成六个可比较的概念方向，由人选择，而不是只给一个答案。
Notes: The same needs can generate several concept strategies for people to compare outlines, support methods, and hard/soft splits. The six left-ear concepts are Seed Pod with a shallow saddle soft support, Pebble with a rounded low profile, Fin Wing with a short wide soft fin, Spiral with a shallow curled surface, Bloom with a soft-gel petal wrap, and Twin Petal with overlapping twin shells. They demonstrate this round's generation flow and have not yet been selected. Volume, comfort, and stability have not been tested, and later selection must keep checking these requirements. Other input features can produce other concept directions.

## Slide 3
Concept Image Inputs, Evidence, and Drawing Plan
Using the Fin Wing direction as an example, this shows how user needs become an executable generation Prompt.
Retrieval and Prompt are archived; data-to-parameter bindings were not saved, so the drawing plan is a review summary.
User input
In-ear, comfortable, biomimetic, moderate size; stable in sport, stays on in sleep, youthful colors.
Split into product form, use scenarios, and look preferences; comfort and stability remain goals to verify.
1 RAG evidence
Real keyword search returned 4 cases
In-ear, comfort, low profile, soft hold
Huawei ear-clip: hard/soft split
Vendor data; cross-form materials
QuietOn sleep plugs: low profile
Vendor data; low volume limits features
2 Drawing plan review
Summarized from the archived Prompt
Fin Wing: oval body + wide soft fin
Blue-gray shell + teal matte soft gel
Assumed: soft fin support limits bulge
Left ear, short-neck tip, shared parts
Left worn, center four views, right hero
3 Assemble the Prompt
Summary of the original English Prompt
One left earbud, 3:2 concept board Oval body + short wide rounded fin Blue-gray shell + teal matte soft gel Shared parts, joints, size, occlusion TOP oblique view, no tall hook or grid
4 Image tool run and review
Tool renders the Prompt; six candidates are checked for consistency, then a person selects.
Candidates: Seed Pod, Pebble, Fin Wing, Spiral, Bloom, Twin Petal.
Check: left-ear side, joints, materials, and views; deviations go back into the Prompt.
以鳍翼方向为例，用户需求经 RAG 依据和画图方案变成可执行的生成指令，工具出图后由人选型。
入耳式、舒适、仿生、体积适中，运动稳定、睡觉不掉，配色年轻。
Notes: This slide takes the user's needs as the example and expands product form, use scenario, and aesthetic preference into execution inputs. The archived real-keyword retrieval for the same needs returned four candidates: the Huawei ear-clip case provides the vendor's description of the hard/soft split, and the QuietOn sleep plugs provide the vendor's description of low protrusion and the trade-off between features and volume; both are kept separate from in-ear performance validation. The Fin Wing plan in the figure is reconstructed from the original generation Prompt and specifies the oval body, the short wide rounded soft fin, the blue-gray hard shell, the teal matte soft gel, the same left ear, shared components, and the required views. The item-by-item binding of data to each drawing parameter was not saved, so the continuous decision log of that time cannot be recreated. The existing results cover six directions. The image tool and RAG are separate steps; after rendering, the ear side, joints, materials, and views still need checking before a person selects. The original retrieval and the full English Prompt are archived; comfort, stability, and engineering dimensions remain to be validated.QuietOnPromptRAGPrompt

## Slide 4
Consistency Rules for Concept Images
Side, layout, and part relations are written into the generation spec, read by templates, RAG prompts, and tests.
Left ear only
Original orientation kept
Six-panel layout
Worn / four views / hero
No other panels are kept
Consistent across views
Shared proportion, joints, materials
Next-round entry points
Spec, references, prompts, tests
Consistency rules apply to new concepts. Form, color, and material follow the task.
概念图的侧别、版式和部件关系写成规则，每一轮生成都按同一标准检查。
Notes: Side, layout, and shared part relations are written into the concept-image generation spec, which is read by the template, the current reference list, RAG prompts, and tests. The current case uses the left ear only and keeps the original orientation, with a six-panel layout: worn view on the left, four views in the center, and the hero image on the right. The four views are side, front, rear, and an angled top view, and only these panels are shown. All views share proportion, joints, and material split, and the review checks each item for consistency. New tasks reuse the consistency check method; form, color, and material are decided by the task, and if the user chooses another side, the new choice applies.

## Slide 5
Questions on AI Collaboration
A continuous design task records AI participation, change feedback, and review results.
Four questions to answer
Is there traceable evidence?
Can it run real tool operations?
Can it locate errors and fix them?
Can the next round read past lessons?
Unit of observation
Feedback, changes, reviews
Methods and corresponding evidence
Methods added
Knowledge retrieval, concept-first, tool links
Process evidence
History images, operation logs, rules, code
Result checks
Save and reopen, shape checks, user review
Lesson reuse
Update workflow and entries, then regression-test
Case observation checks the process. Gains still need controlled validation.
方法论围绕四个问题展开：依据可追溯、工具可执行、错误可定位、经验可复用。
引入的方法：知识检索、概念前置、工具连接
过程证据：历史图、操作记录、规则与代码
结果核查：保存重开、形态检查、用户复核
经验复用：更新工作流和入口，再做回归测试
Notes: This study is organized around four questions: can design evidence be traced, can AI operate real tools, can it locate and fix errors, and can existing lessons be read by the next round. We use feedback, changes, and reviews as the unit of observation, and compare them against the history images, operation logs, rules, and code left by knowledge retrieval, concept-first work, and tool connections. Result checks include reopening after save, shape checks, and user review. Lesson reuse requires updating the workflow and the run entry points, then running regression tests. So far we have process records from a single case. Control groups, efficiency metrics, and wear tests are still pending, and any gains need later controlled validation.

## Slide 6
Design Task Execution and Review Flow
AI analyzes needs and runs the task. People review concepts, major changes, and deliverables.
Input: user description, confirmed constraints, current project state
Structure needs
Traits / conflicts / gaps
Find evidence
Sources and limits
Idea
Comparable options
Human: select
Concept / side / views
Output: needs table
Output: traceable reference pack
Output: concept board
Output: single current reference
Form and model
Parts / ratio / fit
Run real tools
Model / save / reopen
Geometry review
Geometry / angle / limits
Accept
Output: checkable CAD
Output: saved-state receipt
Output: issue list and evidence
Release on acceptance
On a failed review, locate, fix, and recheck. Write back lessons at task close.
Each round first checks the tool connection and resumes after it is restored.
AI 负责分析与执行，人负责选型、重要变更和验收，每一步都有可检查的输出。
Notes: A design task starts from the user description, confirmed constraints, and the existing project state. AI organizes features, conflicts, and unknowns into a needs table, then retrieves references that carry their source and applicable limits, and generates several comparable concept directions. After a person confirms the concept, side, and views, AI analyzes parts, proportions, and attachment, then performs modeling, saving, and an independent reopen. Geometry and visual review produce an issue list and a receipt, and a person accepts the results within that scope. Failed items are traced to a specific step, fixed, and rechecked; release happens only after acceptance. Each round first verifies the current tool connection, and general lessons are updated when the task closes.

## Slide 7
Feature Extraction from User Descriptions
AI extracts design features from the description, retrieves data by need dimension, and organizes candidates.
Natural-language description
Problem, context, preferences
Example input:
in-ear, stable in sport and sleep, youthful colors
Split need dimensions
Form / scene / function / look
Mark constraints, conflicts, open items
Sleep is a scene. In-ear is a form
Retrieve and combine
Query per dimension, then combine
Deduplicate, keep uncovered items
Lexical and semantic search keep sources
Hard constraints
Limits that must hold
Soft preferences
Used for ranking options
To clarify
Ask when sizes are missing
Trial result
After deduplication, two different products cover more needs
Dimension split and coverage selection passed an independent trial. Not yet integrated into the main project. Wear performance untested.
The example shows the method. Users still confirm constraint strength and priorities.
AI 先把用户描述拆成形态、场景、功能和偏好，再按维度检索参考，约束由人确认。
Notes: Feature extraction works from the user description, and the input can be swapped for other needs or product tasks. In-ear, stable in sport, stays in during sleep, and youthful colors is a demo input, where in-ear describes form and sleep describes a scene. AI splits the needs by form, scene, function, and appearance preference, marks hard constraints, soft preferences, conflicts, and items to clarify, and asks for confirmation when sizes or priorities are missing. Retrieval queries by dimension, combines complementary references, deduplicates products, and records uncovered items. Both lexical and semantic retrieval keep their sources. An independent trial used deduplication to choose two different products that cover more needs. Dimension splitting and coverage selection are not yet automatically integrated into the main project. Wear performance is untested, and constraint strength and priorities are still confirmed by the user.

## Slide 8
RAG Knowledge Retrieval and Design Evidence
RAG (retrieval-augmented generation) reads product cases, ear data, and tool docs to ground the design.
Design data: trade-offs
Product cases, images, feedback
Structure, support, materials
Main evidence retrieved for this case
Ear data: constraints
Ear regions, sizes, contact limits
Placement and fit. Comfort untested
Separate knowledge base, chosen per task
Tool data: operations
FreeCAD docs, modeling, checks
Guides operations and checks
Retrieved apart from product design data
How retrieved data supports design decisions
Small-volume cases: simplify functions and structures
Soft-support cases: hard shell vs. contact parts
User feedback: charging, controls, long-term trade-offs
Record advice, evidence, open items
Which features to borrow, and from where?
Which sizes and wear performance lack evidence?
References include QuietOn, Kokoon, Ozlo, and Nothing Ear, each with source type and applicable limits.
Retrieval relevance and source credibility are assessed separately
产品案例、耳部资料和工具文档分库检索，每条建议都带来源和适用限制。
检索资料对设计判断的支持
Notes: RAG stands for retrieval-augmented generation. It brings retrieved material into the current task so that AI can make design suggestions with sources. Here we use three separate knowledge bases: product design, ear anatomy, and tools. Product cases, image observations, and user feedback provide references for structural trade-offs, support methods, and material expression. Ear data provides position, size meaning, and contact constraints. FreeCAD documentation helps choose modeling and check operations. In this case, small-volume products supported function and structure trade-offs, soft-support cases helped separate the hard shell from contact parts, and user feedback added charging, control, and long-term use issues. References include QuietOn, Kokoon, Ozlo, and Nothing Ear, and each suggestion keeps its source type, applicable limits, and open items. Retrieval relevance and source credibility are judged separately, and real comfort still needs wear trials.

## Slide 9
Evidence Review of Retrieved Data
Review source, visible facts, and inference to decide which design conclusions each item supports.
Source records
Vendor notes, reviews, user feedback
Keep author and source category
Image observation
Outline, material zones, accessory relations
Sizes and use effects need other evidence
Inference records
AI inferences recorded separately
Unsupported conclusions marked as open
Review flow before data enters design
01 Verify source
Check original text and image source
Record author and conditions
02 Match purpose
Shape reference or support data
Sizes must map to a specific part
03 Keep open items
File inference apart from source text
Not modeled on weak evidence
An independent trial reviewed 166 images: 119 as shape references, 47 as support data.
Comfort, sport stability, and retrieval quality gains still need separate validation
资料进入设计前先核对出处、区分用途、标记待确认项，依据不足的不用于建模。
Notes: Evidence review records sources, image observations, and AI inferences separately. Vendor notes, independent reviews, and user feedback keep the author and source category. Images can support observations of outline, material zones, and accessory relations, while sizes and use effects need matching evidence. Before data enters the design, we verify the original text and image source and record the applicable conditions, then separate shape references from support data by purpose, and sizes must map to a specific part. Inferences are filed apart from the source text, and conclusions without evidence are marked as open and not yet used for modeling. An independent trial reviewed 166 images one by one: 119 were classed as shape references and 47 as support data. Comfort, sport stability, and retrieval quality gains still need separate validation.

## Slide 10
MCP Tool Calls and Result Checks
MCP connects tools, RAG provides evidence, and people review scope and results.
Human
needs / review
Scope and protections
AI executor
Plan tasks, pick tools, check
Knowledge, confirmed project state
Restore a failed tool link first
Tool interfaces and scope
Headless: docs, scripts, export
Static script check, isolated process, result check
CAD GUI bridge: read / limited edits
GUI prototype supports verified operations only
Real window and document still checked
Result review flow
Save file
Reopen
Shape check
A/B receipt and human review
Failed checks return to execution. Major trade-offs return to design review. People accept the final result.
Interfaces split work by verified capability. Actual files are checked after each operation.
MCP 连接真实工具，AI 执行后保存、重开并出具 A/B 回执，最终结果由人验收。
Notes: MCP connects the tools, RAG provides design evidence, and people review the execution scope and results. AI combines the confirmed project state to organize tasks, choose tools, and check receipts. Tool paths include headless document, script, and export operations, plus the existing CAD GUI bridge; the GUI prototype supports only its verified operations, and the current task still confirms the actual window and document. Scripts are checked before execution, run in an isolated process, and their results are verified afterwards; if the connection fails, it is restored first. After a file is saved it is reopened independently, geometry and visuals are checked, and a comparison receipt is produced for human review. Failed checks return to execution, major design trade-offs return to design review, and a person accepts the final result. Different interfaces divide the work by their own verified capabilities.

## Slide 11
How Review Results Enter the Next Round
Changes run after the plan is confirmed, same-version receipts support human review, and rules re-enter the workflow.
Accepted scope and gaps are recorded separately; after write-back, check actual reads and regression.
Human feedback
Describe, mark, goal
AI restates plan
Edits and protections
Human confirms
Scope and trade-offs
AI applies edit
Save and fresh reopen
Make A/B receipt
Same-setting A/B PDF
Human reviews
Accepted scope, gaps
Accepted scope and open items are logged separately; failed items are reworked.
Receipt of a soft-leaf nudge
After write-back, check the actual reads
Workflow and project memory
Prompts, templates, tool entries
Known pass/fail cases and next task
复核结果写回工作流和项目记忆，下一轮先确认规则被实际读取，再开始任务。
一次软叶微移的实际回执
Notes: Each change starts with human feedback. AI restates the goal, the plan, and the protected items, and implements only after confirmation or under explicit prior authorization. The file is saved and reopened independently, and a same-condition A/B PDF is provided for human review; the accepted scope and unresolved items are recorded separately, and anything that fails is reworked. The right side keeps the actual receipt of one soft-leaf nudge, used only to show the review scope of that change. Effective methods and failure boundaries go into the workflow, project memory, generation prompts, templates, and tool entry points, and known positive and negative cases plus the next task are used to check that they are actually read. Specifications, tool implementation, tests, and migration are tracked separately; write-back does not mean model parameter training or overall product acceptance.AIA/B PDF

## Slide 12
Growth of AI Collaboration: Stages 1 to 3
Concept images come first. Choose the direction, then turn the concept into an editable 3D model.
Six stages grouped by capability. Methods refine each other. Candidates still await review.
1 Rough geometry
Early trial: geometry, thin evidence.
Skill
Needs to rough geometry
Gap
Modeling lacked evidence
Step
Concept first, human pick
Gain
Set direction, then model
2 2D first, then translate
Early 2D outline excerpt. Concept fixed first.
Skill
Compared 2D concepts
Gap
No concept guidance
Step
Concept first, then lock
Gain
Chosen concept to 3D
3 Concept and 3D review
Concept front
Model front
Newer method: one-reference check.
Skill
Editable 3D concept
Gap
Wrong face
Step
Relabel, check sections
Gain
Feedback now checkable
从直接建模到概念图先行，再到概念与 3D 联审，每个阶段补上前一阶段的缺口。
Notes: Early on, AI could turn need words into rough geometry, and direct modeling exposed the lack of form evidence. Concept-first put ideation, 2D expression, and human selection before modeling, locking the design intent first. The gap at the second node was an editable 3D model, so the next stage had to turn the chosen concept into editable CAD geometry. Once the model existed, the concept and the saved model could be checked item by item, while occlusion ambiguity in circled feedback still needed later spatial diagnosis. The early 2D outlines come from the real archive; the later joint-review image is an example of a newer method, and the candidate still awaits review.

## Slide 13
Growth of AI Collaboration: Stages 4 to 6
Real sections and ear-region knowledge aid placement. Whole-unit moves and review write-back support later tasks.
Ear regions and sections support position checks. Wear and cross-task effects are still under validation.
4 Circling and sections
Entry
Near soft leaf
Ear
Tip
Nozzle
Leaf
Real sections, equal scale.
Skill
Sections show depths
Gap
Ear names not on model
Step
Map bound to CN/EN names
Gain
Feedback on ear regions
5 Ear-region placement
Cymba concha
upper concha
Crus of helix
helix root
Cavum concha
lower concha
Names, map, and real source faces match.
Skill
10 regions map to faces
Gap
Local fixes hid bad pose
Step
Align ears, move as unit
Gain
Fit targets guide pose
6 Joint wear and review
Before
After
Real saved state, same-camera A/B.
Skill
Direction partly confirmed
Gap
Joint and wear untested
Step
Review, A/B, write-back
Gain
Traceable, gaps logged
真实剖面和耳区名称让反馈能定位到模型，整机联动和 A/B 复核让修改可追溯。
Notes: Real sections help verify part layers and distances; the two images excerpt 635 independent section lines, each shown at equal scale. Once the ear-region names in Chinese and English, the map, and the real source faces are bound together, feedback can be placed on the model. When the overall pose is wrong, the whole unit and its parts move together, so local deformation stops compensating for layout errors. The saved-state A/B in the image keeps the same camera; the partial confirmation of the unit direction covers only that judgment, and joint, support, and real wear still need validation. Methods that pass review, failure causes, and applicable limits are written back to the workflow and the execution entry points, and cross-task effects keep being checked.

## Slide 14
Progress and Next Validation
Process evidence supports method checks. Cross-task reuse and product performance still need validation.
Used in the main project
RAG, concept-first, tool runs
Reopen, receipts, write-back
Records checkable, product pending
Independent trial results
Form/scene split, coverage pick
Image purpose, size attribution
Not yet fully in the main automatic path
Open questions
Efficiency and quality gains
Comfort, stability, production
Controls and tests still needed
Validation plan for the next round
New needs and product task
Log errors, rework, data gaps
One-standard controls
Check extraction and rule reuse
Track rule reads and failures
Wear tests, engineering tests
Product: pose refinement paused, joint under review, multi-view regression pending, gaps kept.
Method use, user acceptance, product performance, and cross-task validation are recorded separately
流程证据已可核查，效率提升和佩戴性能仍需对照试验和实测验证。
Notes: The main project already uses RAG retrieval, concept-first work, tool execution, save-and-reopen, review receipts, and lesson write-back, and the process records can be checked. Form and scene splitting, need-coverage selection, and the review of image purpose and size attribution have independent trial results but are not yet fully on the main project's automatic path. Causal gains in efficiency and design quality, plus real comfort, stability, material, and manufacturing performance, still need validation. The next round can switch the needs and product task, check feature extraction and rule reuse, log errors, rework, and data gaps, track rule reads and failures, run controls with one standard, and then run wear and engineering tests separately. Pose refinement is paused for now, the joint candidate awaits review, later multi-view and form regression are pending, and earlier gaps are kept. Method use, content acceptance, product performance, and cross-task validation each record their own results.